CopleyControl Class Commands
Commands	Input Type	Output Type	Description
Init	DevVoid	DevVoid	init the device
Move	DevVoid	DevVoid	trigger the motor to move.
SendCommandResult	DevString	DevString	write a command and get the result of this command from the motor controller.
State	DevVoid	State	if the motor is in motion, the State is “MOVING”; / if the motor is stationary, the State is “ON”; / if the motor is out of power, the State is “OFF”;
Status	DevVoid	DevString	if the motor is in motion, the State is “Status is MOVING”; / if the motor is stationary, the State is “Status is ON”; / if the motor is out of power, the State is “Status is OFF”;
Write	DevString	DevVoid	write ASCII message to the controller directly
CheckMove	DevVoid	DevLong	the function returns 1, if the motor is moving.Otherwise returns 0.
CompleteMove	DevVoid	DevLong	waits for the move to be finished, does the backlash, if FlagBacklash
GetPosition	DevVoid	DevDouble	get the defined position
GetRegister	DevVoid	DevLong	returns the controller register contents, hardware
SetRegister	DevLong	DevVoid	loads the motor register with a value, the hardware (to be tested)
ResetMotor	DevVoid	DevLong	reset the motor
StartMove	DevVoid	DevLong	a motor with FlagMotorReady is started, the function returns immediately
StopMove	DevVoid	DevLong	stop a movement immediately. (to be tested)
MoveToCwLimit	DevVoid	DevLong	Moves the motor until the CW limit is reached (positive step direction). Software limits are ignored. StopMove works.
MoveToCcwLimit	DevVoid	DevLong	Moves the motor until the CCW limit is reached (negative step direction). Software limits are ignored. StopMove works.

CopleyControl Class Attributes
Attributes	R/W type		Data type	Value, Range, Unit	Description
Acceleration	READ_WRITE		DevDouble	Units: 10 counts/s2	the acceleration
Deceleration	READ_WRITE		DevDouble	Units: 10 counts/s2	the deceleration
NodeID	READ		DevShort	Range: 0-127	the CAN node address
Port	READ		DevString	Default value: “/dev/ttyS0”	the serial port
Position	READ_WRITE		DevDouble	Units: Counts	the relative position
Velocity	READ_WRITE		DevDouble	Units: 0.1 counts/s	the velocity
State	READ		State		device state. / if the motor is in motion, the State is “MOVING”; / if the motor is stationary, the State is “STANDBY”; / if the motor is out of power, the State is “OFF”;
Status	READ		DevString		device status. / if the motor is in motion, the State is “Status is MOVING”; / if the motor is stationary, the State is “Status is ON”; / if the motor is out of power, the State is “Status is OFF”;
FlagBacklash	READ		DevLong		It shows always 0 if the motor is not moving or a backlash will not be added at the end of the started movement. / (Internally set to 1 if a backlash compensation will be performed at the end of the current movement.)
FlagMotorReady	READ		DevLong		It shows always 0 if the motor is not moving. / If the motor is in motion, returns 1.